## Slide 1: US 2020 Energy Market Value
Reference Case
Miles Evans
08/05/2021

## Slide 2: Case Description
Value of Energy Shifting
Hub-level across United States ISO/RTO regions
Energy time shifting only
Very simple storage model
  85% roundtrip efficiency
  Variable duration (2-96 hours)
  No auxiliary load, self discharge, minimum power, etc.

## Slide 3: Setup
Install command line version of DER-VET and StorageVET as a sub-module
Download Reference Case .zip file and extract contents
Move model parameters files to dervet folder
Move run_all.bat to dervet folder
Move timeseries data files to dervet\storagevet\data\Timeseries Files
Move other data files to dervet\storagevet\data
Run all cases at once with run_all.bat file on Windows
  Open anaconda prompt
  cd to dervet directory
  Activate DER-VET virtual environment
  Type “run_all.bat” and hit enter

## Slide 4: Results

## Slide 5: Results
10
200.0
Assuming 10yr life and 7% discount rate

## Slide 6: Conclusion
No capacity value or other services (note, ERCOT is included)
  Future work could add in capacity value, where applicable
Only looked at one historical year of data (2020)
  Future work could bring in projections
Only highly simplified Li-ion reference specs were used
  Longer lived, lower efficiency technology options would be interesting, especially for the longer durations.
  More detailed technology specs could improve results